## Slide 1
AI-Assisted Feature Addition To Existing Code
Generative AI Use Case 2 • Ben Reese
Tool: Claude Code (Anthropic CLI agent)
A 30-minute session converting a fixed-point PID controller
to floating point — across VHDL, Python, and build infrastructure.
• ~800 lines of production code generated
• 15 files created/modified
• FPGA firmware + Python drivers + build system

## Slide 2
The Task
Converting a Fixed-Point PID Controller to Floating Point
The system:
• FPGA-based detector readout (VHDL + Python control software)
• PID servo module: ~1000 lines of VHDL, 8 parallel instances
• Goal: replace fixed-point math with IEEE 754 float32
→ Better dynamic range, simpler coefficient tuning
→ Reuse Xilinx FP IP cores already in the design
Why this is a good AI-assisted task:
• Not greenfield — must integrate into a large existing codebase
• Crosses firmware (VHDL) and software (Python) boundaries
• Requires understanding existing design before writing new code
• Many files touched, but the design work is the hard part
[Screenshot: AdcDsp.vhd — existing fixed-point PID] PID_P_S: v.pidResult := resize( r.pidResult + (r.pidCoef * r.pidMultiplier), v.pidResult); v.pidCoef := iSfixed; v.pidMultiplier := r.sumAccum; v.state := PID_I_S;

## Slide 3
The Workflow
Claude Code operates in the terminal alongside your normal dev tools
1. Explore — Agent reads codebase, understands architecture
2. Plan — Proposes approach, asks clarifying questions
3. Implement — Writes code across multiple files
4. Iterate — Responds to feedback, fixes issues
5. Document — Creates plan docs and progress tracking
~30 minutes of interaction for a feature that would
take a day or more by hand.
[Screenshot: Terminal showing initial prompt] $ claude > Let's focus on the > ColumnFpgaBoard325Coordinator10G target. > The AdcDsp block implements a fixed-point > PID. I'd like to adapt it to use floating > point math. The design already has some FP > IP cores. Make a plan. I'll explore the codebase to understand the existing floating point infrastructure...

## Slide 4
AGENTS.md — Giving the Agent Context
The single most impactful thing you can add to a repo for AI assistance
A Markdown file at the repo root:
• Architecture and data flow
• Where to find things (file/directory map)
• Naming conventions and coding patterns
• How to start for each task area
• Build system patterns
Without → agent guesses for many turns
With → immediate navigation, correct
conventions from the start
── AGENTS.md ──
### Data Flow (Column Board)
AD9681 ADC → DataPath → AdcDsp (PID) → EventBuilder → Host
↕
FastDacDriver (SQ1 feedback)
| Task Area | Start With These Files |
|─────────────────|────────────────────────────────────|
| DSP / data path | DataPath.vhd, AdcDsp.vhd, |
| | BiquadFilter.vhd, EventBuilder.vhd |
## Firmware Conventions
- Generics suffixed _G (e.g., TPD_G, SIMULATION_G)
- Constants suffixed _C (e.g., AXIL_CLK_FREQ_C)
- Architecture always named `rtl`
For substantial feature work, keep planning, progress,
and handoff Markdown under docs/plans/<task-name>/.

## Slide 5
AGENTS.md → Plan Docs
Agent automatically created docs/plans/fp-dsp-pid/PLAN.md
Why plan docs matter:
• Plans survive context resets
→ agent resumes in new sessions
• Engineers review before code
→ catch issues early
• Decisions + rationale captured
→ not buried in chat logs
This example fit in one session.
Most features won't — plan docs
become essential for continuity.
── docs/plans/fp-dsp-pid/PLAN.md ──
# Floating-Point PID (AdcDspFp)
## Scope
New module, port-compatible with AdcDsp,
selectable via USE_FLOAT_PID_G generic.
## Architecture
| Core | Operation | Latency |
|--------|-------------|----------|
| FpMac | A*B+C | 4 cycles |
| Int2Fp | int → float | 2 cycles |
| Fp2Int | float → int | 2 cycles |
## Key Design Decisions
1. Track unwrapped feedback value as
primary state (simplifies flux jump)
2. Pass float directly to downstream
filter (skip redundant conversion)
3. Iterative flux jump loop
(handles multi-quantum jumps)
## State Machine (~38 cycles common case)
ACCUMULATE → Int2Fp → P_FMA → I_FMA →
D_DIFF_FMA → D_FMA → SQ1FB_ADD_FMA →
DERIVE_WRAPPED → Fp2Int → FLUX_CHECK →
ANTI_WINDUP → SUM_UPDATE → DATA_STREAM

## Slide 6
Plan → Iteration
The plan evolved through back-and-forth design dialogue
"New module or modify in place?"
→ New file + generic to select
"Can we pass float directly to the next filter stage?"
→ Yes — added bypass generic, eliminates 8 redundant conversions
"How does anti-windup work in float domain?"
→ Sign-bit comparison, no extra FP operation needed
"Support multi-quantum flux jumps?"
→ Iterative integer loop, widened counter from 9 to 16 bits
The agent participates in design — but the engineer
makes the architectural calls.
[Screenshot: Plan mode Q&A in terminal] ┌ Question ─────────────────────────┐ │ Should we create a new module │ │ (AdcDspFp.vhd) or modify AdcDsp │ │ in place? │ │ │ │ ● New module (AdcDspFp.vhd) │ │ ○ Modify in place with generic │ │ ○ Modify in place, replace │ └────────────────────────────────────┘

## Slide 7
Implementation Output
All created/modified in one ~30 minute session
Created:
AdcDspFp.vhd — 600-line FP PID module
Fp2Int.xci — Xilinx IP core (float→int)
_AdcDspFp.py — Python register driver
Modified:
DataPath.vhd — generate blocks
BiquadFilter.vhd — float bypass
WarmTdmPkg.vhd — stream config
ColumnFpgaBoard — top generic
ruckus.tcl — IP loading
+ 7 Python files — CLI + SW stack
~800 lines of production code
all following existing conventions.
── firmware/common/warm_tdm/rtl/AdcDspFp.vhd ──
-- AdcDspFp.vhd (generated)
when PID_P_S =>
if (fpMacOutValid = '1') then
v.pidResultFp := fpMacOutData;
-- I term: result += I * sumAccum
v.fpMacInValid := '1';
v.fpMacA := r.sumAccumFp;
v.fpMacB := r.iCoef;
v.fpMacC := fpMacOutData;
v.state := PID_I_S;
end if;
when PID_I_S =>
if (fpMacOutValid = '1') then
v.pidResultFp := fpMacOutData;
-- D error: lastAccum - accumError
v.fpMacInValid := '1';
v.fpMacA := r.accumErrorFp;
v.fpMacB := X"BF800000"; -- -1.0
v.fpMacC := r.lastAccumErrorFp;
v.state := PID_D_DIFF_S;
end if;

## Slide 8
What Worked / What Needed a Human
Agent handled well:
• Reading & comprehending large existing codebase
• Following established patterns (copied style from BiquadFilter)
• Cross-domain work (VHDL ↔ Python ↔ TCL build system)
• Responding to design feedback and updating coherently
• Auto-generating plan documentation
Required human judgment:
• Architecture decisions (new module vs. modify in place)
• Algorithm correctness (anti-windup semantics, thresholds)
• Catching missed conventions (review found missing patterns)
• Deciding what to test and how to verify
The AI accelerates implementation;
the engineer owns the design.
[Screenshot: Review catch in terminal] > _AdcDsp.py has P_CoefRaw, I_CoefRaw > and D_CoefRaw. The new FP version > only has I_CoefRaw. Why? In the original, all three use the Raw/Link pattern... I simplified P and D. Should I add Raw/Link for all three for consistency? → Add Raw/Link for all three

## Slide 9
Practical Tips
1. Write an AGENTS.md
Biggest ROI for AI-assisted development
2. Use plan mode
Get alignment on approach before code is generated
3. Iterate on design
Treat it as a conversation, not a one-shot prompt
4. Review everything
Fast code still needs the same scrutiny
5. Track plans in the repo
Enables multi-session work and handoffs
6. Stay in your domain
The agent is a force multiplier, not a substitute